## Slide 1: Blue Tooth Technology
“BLUETOOTH represents a single chip,low cost radio based network technology”
Provides Wireless interconnections between low power, short range, small mobile devices (Palmtops, Laptops, PDAs, phones, etc) in close proximity (within a room, car, cabin, elevator…)

## Slide 2: Objectives of Bluetooth Technology
removal of messy wires, providing freedom from wires
Creation of Adhoc piconets and Personal Area Networks(PAN) with limited coverage (within the range of 10 ms)
Infrastructure-less networks without using Switches, Access Points, hubs, routers, etc.

## Slide 3: Blue tooth consortium
Formed by 5 companies in 1998
- Ericsson
Intel
IBM
Nokia
Toshiba
Blue-tooth standard is embraced by over 1000 manufacturers of electronics appliances (Akai, Motorola, LG, Samsung, Nokia, for music, video, data, fax m/c ……)
Blue tooth Special Interest Group (SIG) worked together to develop an integrated voice/data/images (mm) wireless networking

## Slide 4: BLUETOOTH
Named after king Harold Blatand who was born in 10th Century and united Denmark and Norway.
1. Features
- Operates at 2.4.GHz ISM license-free band (2400-2483.5 MHz.)
- Devices connected using bluetooth RF link form a PICONET
2. Bridging of networks:
piconet WLAN Wired LAN
piconet GSM WAP Server

## Slide 5: Applications of Bluetooth Technology
Connects Keyboard, mouse, printers, headphones, head sets with speakers etc. to PC without wires.
To Interconnects hand held, portable, battery operated devices like mobile phones, hands free equipment with mobile phones, PDAs, mobile computers, communicators,, microphones, wireless speakers to home theatre systems

## Slide 6
Scanner
Printer
Speakers
Joystick
The Bluetooth wireless computer model

## Slide 7: The Bluetooth interactive conference (file and object transfer)

## Slide 8: Blue-Tooth Architecture
Bluetooth Technology Protocols are implemented using following layered Architecture:-
Physical Layer
MAC Layer
Network Layer
Security
Link Management

## Slide 9: Design issues of physical Layer
1. Power consumption should be very low due to battery operated devices. LOW Power states used.
2. Freq. Band (2400-2483.5 MHz) 83.5MHz. B.W.
3. Fast Freq. Hopping TDD scheme at a rate of 1600 hops/sec. to avoid narrow band interference
4. Within a Pico net all devices use the same hopping sequence
5. Transmitter Power upto 100mW.
6. Range 10m-100m with special transceivers.
Notes: Time division duplex (TDD) refers to duplex communication links where uplink is separated from downlink by the allocation of different time slots in the same frequency band. It is a transmission scheme that allows asymmetric flow for uplink and downlink data transmission.
A piconet is an ad hoc network that links a wireless user group of devices using Bluetooth technology protocols. A piconet consists of two or more devices occupying the same physical channel (synchronized to a common clock and hopping sequence).

## Slide 10: Low Power States
Park State : Lowest Power Consumption
Listens to traffic of master device to resynchronize & check for broadcast messages. Device releases MAC address
Hold State: Higher Power Consumption
Device does not release its MAC address and can resume transmission once out of hold.
SNIFF State : Highest Power Consumption
The device holds MAC address listens to the piconet at regular interval at a reduced rate which is programmable and application dependent.

## Slide 11: MAC Layer (Channel Access)
“A piconet is a centralized TDM system with the master controlling the clock and determining which device gets to communicate in which time-slot(polling).”
One device acts as master
Other devices (upto seven act as slaves)
Master determines the hopping sequence
MAC address (001-111) is assigned to each device in the piconet for polling.
Notes: In electronic communication, 'polling' is the continuous checking of other programs or devices by one progam or device to see what state they are in, usually to see whether they are still connected or want to communicate.
Time-division multiplexing (TDM) is a method of putting multiple data streams in a single signal by separating the signal into many segments, each having a very short duration. Each individual data stream is reassembled at the receiving end based on the timing.

## Slide 12: Master device identity
Each packet exchanged over channel within the piconet possesses this access code which identifies the master and is passed on at the time of connection establishment.
Packet format
Access Code
Packet header
Payload
72
54 bits
0-2745 bits
Notes: When data is sent over the Internet, each unit transmitted includes both header information and the actual data being sent. The header identifies the source and destination of the packet, while the actual data is referred to as the payload.

## Slide 13: Services offered at MAC Layer
Synchronous Connected Oriented Link (SCO)
for telephone calls for uninterrupted voice signal tx.
symmetrical, circuit switched, point-to-point connections.
Asynchronous Connection less Link (ACL)
for data transmission e.g. Web traffic
asymmetrical or symmetrical, packet switched
point to multipoint transfer (broadcast, multicast)

## Slide 14: Bluetooth Scatter-net
All users within one piconet have the same hopping sequence and share the same channel
Many piconets with overlapping coverage can exist simultaneously.
Each piconet has a unique hopping sequence and one device can participate in more than one piconet.
“The group of PICONET within the same geographical area is called a scatter net”.

## Slide 15
Scatternet
piconets

## Slide 16
Vulnerable to security attacks and threats Blue tooth offers a mechanism for
Authentication & (one-way, two-way authentication)
Encryption at MAC layer (higher layer and at Chip level)
Key length of 0,40, 64 used for encryption.
Security

## Slide 17: Security Modes
Security Mode 1: non-secure
(open to all devices)
Security Mode 2: service level enforced security (encryption)
Security Mode 3:Link level enforced security
(authentication & authorization)

## Slide 18: Methods for illegal access
Bluejacking
  Anonymous business cards with undesired messages sent to devices within 10 mts. Range (inquiry/ping)
Bluebugging
  allows hacker to initiate phone calls, send and receive text messages and eavesdrop phone conversation and connect to the Internet

## Slide 19: Link Management
Link Manager Protocol (LMP)
- Handles authentication
negotiates authentication parameters (e.g. packet size, buffer space, etc.)
encryption
controls the power modes of each device (i. e. park, hold, sniff.)

## Slide 20: Link Management Protocols
Logical Link Control Adaptation Protocol(L2CAP)
Packet fragmentation, Frame formation
Multiplexing & Demultiplexing of packets received from different sources
QOS:- (1) Maximum payload size negotiated
(2) Flow control
Base band enables RF link between Blue-tooth units
- Inquiry
- Paging Signals generated

## Slide 21: THE BLUETOOTH FRAME FORMAT
Access Code: Identifies the master
Addr.: Identifies the slaves (001-111)
Type: Frame type (ACL,SCO, Null etc.)
Length of frame (no. of slots)
A : Piggybacks Acknowledgement to a frame
F : Flow bit asserted by a slave when buffer is full
S : Sequence no.
Check sum: Error control using CRC.
Access Code
Header
Data (Payload)
Addr.
Type
F
A
S
Checksum
72
54
0-2744
bits
3
4
1
8
1
1
10+8=18

## Slide 22: THE BLUETOOTH PROTOCOL STACK
RF Comm: a serial emulation Protocol to implement RS-232 Serial port. Allows connection of legacy devices like keyboard, Mouse, Modems to PC.
TCS (Telephony Control Protocols) used for the three speech oriented profiles:-
  Cordless Telephony
  Intercomm (Walkie Talkie)
  The Headset profile provides hands free voice comm. Between mobile phone and head set (Cordless)

## Slide 23: The Application Layer
Supports profile and applications for
- LAN access (mobile computer fixed LAN)
- Fax (mobile phone to mobile fax)
- Synchronization (PDA to computer)
- File transfer facility
Dial-up Networking (notebook to mobile phone)

## Slide 24: Conclusion
Robust Foundation
Industry Backing
A detailed specification
Dedicated product developers worldwide
Bluetooth technology is a major influence in wireless communication and connections
Visit www.bluetooth.com for detailed information

## Slide 25
THANK YOU